## Slide 1
ICT LAB TOPIC:
Computer Architecture

## Slide 2: What computer does do?
 The processor can read and write items in the memory according to some list of instructions, while the memory simply remembers the data it has been given. The list of instructions executed by the processor are known as
a computer program.
Basically, a machine is universal if it is able to do the following:
 Read a value from memory.
 Based on the read value, determine a new value to write to memory.
 Based on the read value, determine which instruction to execute next.

## Slide 3: Computer Architecture
 Computer architecture describes how a machine is logically
organized and how its instruction set is actually implemented.
 One of the most important architectural decision made in designing a computer is how its memory is organized, and how programs are loaded into the machine.
 In the early history of computers, there was a distinction between
stored program and hardwired computers.
 Rewiring a machine simply takes too long when compared to the process of simply loading new data into the machine.
 In the current era of computing, almost all computers are stored program computers. In this book, we will be focusing on stored program computer architectures.

## Slide 4: Continue..
 The main features of computer system are −
 Development of true artificial intelligence
 Development of Natural language processing
 Advancement in Parallel Processing
 Advancement in Superconductor technology
 More user-friendly interfaces with multimedia features
 Availability of very powerful and compact computers at cheaper rates
 Some computer types of this generation are −
 Desktop
 Laptop
 Note Book
 ChromeBook

## Slide 5: Types Of Computer Architecture
Von Neumann Architecture
Harvard Architecture

## Slide 6: Von Neumann Architecture
 The invention of stored program computers has been ascribed to a mathematician, John von Neumann, who was a contemporary of Mauchley and Eckert.
 Stored-program computers have become known as Von Neumann Architecture systems.
 Today’s stored-program computers have the following characteristics:
 Three hardware systems:
A central processing unit (CPU)
A main memory system
An I/O system
 The capacity to carry out sequential instruction processing.
 A single data path between the CPU and main memory.
 This single path is known as the von Neumann bottleneck.

## Slide 7: Von Neumann Architecture
 The Von Neumann Architecture is, by far, the most common architecture in existence today. PCs, Macs, and even Android phones are examples of Von Neumann computers.
 There is a bus (address bus/data bus/control bus) used for the instruction and data code execution.

## Slide 8: Harvard Architecture
 Harvard architecture is used when data and code is present in different memory blocks.
 A separate memory block is needed for data and instruction.
 Data can be accessed by one memory location and instruction can be accessed by a different location.
 It has data storage entirely contained within the central processing unit (CPU). A single set of clock cycles is required.
 We can observe in the below image, there are separate data and instruction memory that is a bus available
to perform operations.

## Slide 9: CA v/s CO
Computer Architecture | Computer Organization
Computer Architecture is concerned with the way hardware components are connected together to form a computer system. | Computer Organization is concerned with the structure and behaviour of a computer system as seen by the user.
It acts as the interface between hardware and software. | It deals with the components of a connection in a system.
Computer Architecture helps us to understand the functionalities of a system. | Computer Organization tells us how exactly all the units in the system are arranged and interconnected.
A programmer can view architecture in terms of instructions, addressing modes and registers. | Whereas Organization expresses the realization of architecture.
While designing a computer system architecture is considered first. | An organization is done on the basis of architecture.
Computer Architecture deals with high-level design issues. | Computer Organization deals with low-level design issues.
Architecture involves Logic (Instruction sets, Addressing modes, Data types, Cache optimization) | Organization involves Physical Components (Circuit design, Adders, Signals, Peripherals)

## Slide 10: The Computer Level Hierarchy
 Each virtual machine layer is an abstraction of the level below it.
 The machines at each level execute their own particular instructions, calling upon machines at lower levels to perform tasks as required.
 Computer circuits ultimately carry out the work.

## Slide 11: The Computer Level Hierarchy
 Level 6: The User Level
 Program execution and user interface level.
 The level with which we are most familiar.
 Level 5: High-Level Language Level
 The level with which we interact when we write programs in languages such as C, Pascal, Lisp, and Java.

## Slide 12: The Computer Level Hierarchy
 Level 4: Assembly Language Level
 Acts upon assembly language produced from Level 5, as well as instructions programmed directly at this level.
 Level 3: System Software Level
 Controls executing processes on the system.
 Protects system resources.
 Assembly language instructions often pass through Level 3 without modification.

## Slide 13: The Computer Level Hierarchy
 Level 2: Machine Level
 Also known as the Instruction Set Architecture (ISA)
Level.
 Consists of instructions that are particular to the architecture of the machine.
 Programs written in machine language need no compilers, interpreters, or assemblers.

## Slide 14: The Computer Level Hierarchy
 Level 1: Control Level
 A control unit decodes and executes instructions and moves data through the system.
 Control units can be micro programmed or hardwired.
 A micro program is a program written in a low-level language that is implemented by the hardware.
 Hardwired control units consist of hardware that directly executes machine instructions.

## Slide 15: The Computer Level Hierarchy
 Level 0: Digital Logic Level
 This level is where we find digital circuits (the chips).
 Digital circuits consist of gates and wires.
 These components implement the mathematical logic of all other levels.

## Slide 16: Basic System Architecture
 The processor alone is incapable of successfully performing any tasks. It requires memory (for program and data storage), support logic, and at least one I/O device (“input/output device”) used to transfer data between the computer and the outside world.
 The basic computer system architecture is shown

## Slide 17: Processor
 The processor is the most important part of a computer, the component around which everything else is centered.
 In essence, the processor is the computing part of the computer.
 A processor is an electronic device capable of manipulating data (information) in a way specified by a sequence of instructions.
 The instructions are also known as opcodes or machine code .
 This sequence of instructions may be altered to suit the application, and, hence, computers are programmable. A sequence of instructions is what constitutes a program.

## Slide 18: Memory
 Memory is used to hold data and software for the processor.
 There is a variety of memory types, and often a mix is used within a single system. Some memory will retain its contents while there is no power, yet will be slow to access.
 Other memory devices will be high- capacity, yet will require additional support circuitry and will be slower to access.
 Still other memory devices will trade capacity for speed, yielding relatively small devices, yet will be capable of keeping up with the fastest of processors.

## Slide 19: Types of Main Memory

## Slide 20: Continue
 RAM
 It is where the processor may easily write data for temporary storage. RAM is
generally volatile, losing its contents when the system loses power.
 SRAM
 SRAMs use pairs of logic gates to hold each bit of data. SRAMs are the fastest form of RAM available, require little external support circuitry, and have relatively low power consumption.
 Their drawbacks are that their capacity is considerably less than DRAM, while being much more expensive.
 DRAM
 DRAMs are the highest-capacity memory devices available and come in a wide.
 Most processors with large address spaces include support for DRAMs.

## Slide 21: Continue
 ROM
 ROM stands for Read-Only Memory.
 ROMs are nonvolatile memory, requiring no power to retain their contents.
 They are generally slower than RAM, and considerably slower than fast static RAM.
 The primary purpose of ROM within a system is to hold the code (and sometimes data)
that needs to be present at power-up
 EPROM
 Short for Erasable Programmable Read-Only Memory, EPROM is a non-volatile memory chip that can only be read.
 PROM
 PROM stands for Programmable Read-Only Memory, during the manufacturing process, a PROM is manufactured in an empty state and then programmed later using a PROM programmer or burner.
 EEPROM
 EPROM stands for Electrically Erasable Programmable Read-Only Memory, and the distinction between EPROM and EEPROM is that the latter can be erased and written to by the computer system it is installed in.

## Slide 22: Input/output
 The address space of the processor can contain devices other than memory.
 These are input/output devices (I/O devices, also known
as peripherals ) and are used by the processor to communicate with
the external world.
 Some examples are serial controllers that communicate with keyboards, mice, modems, etc.; parallel I/O devices that control some external subsystem; or disk-drive controllers, video and audio controllers, or network interfaces.